## Slide 3: Developing risk and vulnerability assessments
Mark de Bel
Identifying hotspots and investment preparation for climate proof road assets in the Western Balkans
Naam Achternaam

## Slide 4: Table of contents
General Methodology
  Risk assessment
  Climate Change
  Damage and losses
Economic analysis of road assets in Albania
  Approach for Landslides
  Vulnerability
  Measures
  Cost Benefit Analysis and Action perspective
Lessons learned

## Slide 5: Basic Concepts
Naam Achternaam
Notes: Primero daré una introducción a lo que son los modelos de circulación global y cómo el modelado climático funciona

## Slide 6: Effects of climate change on infrastructure design
In general we know whether precipitation or temperature influences the engineering design.
  For example: More intense rainfall may result in more landslides because saturation of soils on slopes
Webinar : Developing risk and vulnerability assessments

## Slide 7: General Methodology
Naam Achternaam
Notes: Primero daré una introducción a lo que son los modelos de circulación global y cómo el modelado climático funciona

## Slide 8: General Methodology
Hazard assessment
Exposure assessment
Vulnerability assessment
Impact assessment
Risk profile
Action perspective
From vulnerability assessment to action perspective
Webinar : Developing risk and vulnerability assessments

## Slide 9: Hazard and vulnerability
Hazard assessment
Exposure assessment
Vulnerability assessment
Impact assessment
Risk evaluation
Action perspective
Webinar : Developing risk and vulnerability assessments
Notes: Risk Analysis: determine where hazards may affect the roads, how big the impact is and what is the probability
Identify and characterize hazards
Determine exposure based on various Return Periods (RP)
Vulnerability based on damage functions
Losses based on recovery functions
Risk expressed as Expected Annual Damage (EAD) and Expected Annual Losses
2. Action planning: determine where to take measures, which measures to take and formulate action plan
Prioritize locations through combination of criticality and risk
Determine measures (interventions/strategies) and their evaluation
Action plan combines prioritized locations, measures and the interventions in time

## Slide 10: Risk profile road network; Damage and Losses
Cost of increased travel time
Cost of increased travel distance
Traffic intensity
Origin
+
Total losses
x
Destination
Risk  AED = repair costs + economic losses
Hazard assessment
Exposure assessment
Vulnerability assessment
Impact assessment
Risk profile
Action perspective
Damage
  Damage to road assets (repair costs)
Losses
  Vehicle Loss Hours as a result of traffic jams on segment
  Vehicles Loss Hours because of alternative routes
Webinar : Developing risk and vulnerability assessments

## Slide 11: Considering climate change
Likelihood
Impact
Webinar : Developing risk and vulnerability assessments

## Slide 12: Considering climate change
Likelihood
Impact
Webinar : Developing risk and vulnerability assessments

## Slide 13: Effects of key uncertainties in external factors
Traffic
Climate change
Low-scenario
High-scenario
Low-scenario
High-scenario
Damages
Losses

## Slide 14: Case study in Albania
Naam Achternaam
Notes: Primero daré una introducción a lo que son los modelos de circulación global y cómo el modelado climático funciona

## Slide 15: Approach – Risk analysis and action planning
Risk analysis per hazard
Hazard mapping (example; floods)
Risk analysis  Annual Expected Damages (AED)
Action planning per hazard
Prioritization of locations
Criticality
Identification of measures
Cost effectiveness analysis (selection of measures)
B/C ratio
Webinar : Developing risk and vulnerability assessments

## Slide 16: Landslides
Notes: Landslide; The downward movement of a mass of rock, earth, or artificial fill on a slope, often induced (started) by prolonged or heavy rainfall.

## Slide 17: Landslides
Vulnerability
Colours indicate probability of a landslide (Low, High)
Based on:
  Historic events
  Susceptibility map
Indicates location proposed measures

## Slide 18: Landslides - Typical measures
Retaining structures e.g. retaining walls, gabion walls
Stepped slope embankments
Internal slope reinforcement e.g. rock bolts
Drainage
Reforestation
(Improved) regular/ preventative maintenance
Better response/ repair plan (i.e. shorter response times)

## Slide 19: Landslide - Measures
Proposed measures per corridor, based on:
Vulnerability
Terrain conditions

## Slide 20: Landslides - Cost Benefit Analysis
Based on CBA:
Assuming measures will reduce AED by 50 %, over 25 years at 4 % net discount rate as benefit, and a traffic growth of 4 %
Corridors 5 and 6, positive decision on investments
Corridors 13 and 14, negative decision on investments

## Slide 21: Criticality
Criticality determined during workshop with local stakeholders.
Take into account, importance for:
International connections
Industry
Harbour
Tourism
Evacuation
Webinar : Developing risk and vulnerability assessments

## Slide 22: Action plan
Webinar : Developing risk and vulnerability assessments

## Slide 23: Lessons learned 1
Desktop studies based on global data with coarse traffic data (corridor level) can produce useful and objective (strategic) results at a network level
  Results are a first scan at network level
  View input and results in this context
  Strategic assessment, not possible to downscale
  Field validation is required for next steps (execution of action plan)
  Are identified locations indeed vulnerable?
  Does cost estimate of measure fit with location?
  Update CBA if needed
Webinar : Developing risk and vulnerability assessments

## Slide 24: Lessons learned 2
Sometimes difficult to find reliable input and data
  Damage functions
  Historical data (for validation)
  Repair costs, downtimes, cost of measures per corridor
  difference between ‘official input’ and ‘realistic input’
National input very important
  Local partners are vital (network, experience and validation)
  Interaction with local stakeholders (e.g. workshops)
Webinar : Developing risk and vulnerability assessments

## Slide 25
Questions

## Slide 26: Contact
facebook.com/deltaresNL
linkedin.com/company/deltares
@deltares
@deltaresNL
www.deltares.nl
Mark.deBel@deltares.nl
@deltares
@deltares
linkedin.com/company/deltares
facebook.com/deltaresNL